| Title | Apply primers and adhesives to tile substrate on site |
| --- | --- |
| Level | 4 | Credits | 14 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of primers and adhesives used for floor and wall tiling, select primers and adhesives, mix primers and adhesives on site, apply primers and adhesives to tile substrate on site, and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Floor and Wall Tiling |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

- Definitions

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Working drawings refers to the set of drawings associated with a construction project, and can include plans, elevations, sections, details or any other drawings that give information about the project.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	For all on-site unit standards the practical assessment evidence must be provided in the context of commercial business construction operations, in the workplace, under normal workplace conditions.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to work unsupervised, demonstrating knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

4	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Resource Management Act 1991;

AS 3958.1:2007, Ceramic tiles - Guide to the installation of ceramic tiles; available from https://www.saiglobal.com/pdftemp/previews/osh/as/as3000/3900/3958.1-2007.pdf.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of primers and adhesives used for floor and wall tiling.

Range	cement-based (one-pot, two-pot, three-pot), acrylic based (one-pot, two-pot).

Performance criteria

1.1	Primers and adhesives used for floor and wall tiling are identified by types and their uses.

1.2	Procedures for mixing tile primers and adhesives are explained in accordance with manufacturer’s specifications.

1.3	Procedures for applying tile primers and adhesives are explained in accordance with the manufacturer’s specifications and work site practice.

Outcome 2

Select primers and adhesives.

Range	primers and adhesives include – cement-based, acrylic-based, one-pot adhesive, two-pot adhesive, three-pot adhesive;

evidence of two types of primers and two types of adhesives is required.

Performance criteria

2.1	Type of substrate is identified from working drawings and site inspection.

2.2	Primers and adhesives are selected in accordance with job specifications and tile type.

Outcome 3

Mix primers and adhesives on site.

Range	manually, mechanically.

Performance criteria

3.1	Primers and adhesives are mixed in accordance with manufacturer’s specifications.

3.2	Safety procedures specified for type of primer and adhesive are followed in accordance with work site practice.

Outcome 4

Apply primers and adhesives to tile substrate on site.

Range	primers and adhesives include – cement-based, acrylic-based, one-pot adhesive, two-pot adhesive, three-pot adhesive;

evidence of two types of primers and two types of adhesives is required.

Performance criteria

4.1	Primers and adhesives are applied in accordance with manufacturer’s specifications.

  - Safety procedures specified for type of primer and adhesive are followed in accordance with work site practice.

Outcome 5

Complete work operations.

Performance criteria

5.1	All operations are safely completed; workplace, tools, plant and equipment are cleaned; and tools, plant and equipment are stored in accordance with work site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 16 December 2005 | 31 December 2024 |
| Review | 2 | 18 February 2011 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.