| Title | Check framing, set up, flash, measure, cut and fix fibre cement board for Proprietary Plaster Claddings on site |
| --- | --- |
| Level | 3 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: check framing on site for suitability for the fixing of fibre cement substrate; describe work necessary to allow the fixing of fibre cement board; set up the work area and plan workflow; identify and fix flashings; and measure, cut, and fix fibre cement board. |
| --- | --- |

| Classification | Construction Trades > Proprietary Plaster Cladding Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Access equipment, for the purpose of this unit standard, means equipment used to facilitate access to the work area, and may include ladders, working platforms, scaffolding or mechanical plant.  Approved codes of practice relating to the safe operation of this equipment are available at https://www.worksafe.govt.nz/.

On site refers to a wide range of building and construction environments within which the Proprietary Plaster Cladding Systems trade skills are applied.

Plant is used as in the Health and Safety in Employment Act 1992 to mean appliances, equipment, fittings, furniture, implements, machines, machinery, tools, vehicles, plus parts, controls, and anything connected.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

2	Legislation, regulations, codes and standards relevant to this unit standard may include:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Hazardous Substances and New Organisms Act 1996; Building Act 2004;

New Zealand Standards, NZS 4218:2004 Energy efficiency – Small building envelope and NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz);

New Zealand Building Code;

Approved Code of Practice for the Safe Erection and Use of Scaffolding (Wellington: Occupational Safety and Health Service, Department of Labour, 1995) available at https://www.worksafe.govt.nz/;

Territorial Authorities’ building regulations.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Check framing on site for suitability for the fixing of fibre cement substrate.

Performance criteria

1.1	Condition of framing is checked on site for suitability for fixing of fibre cement substrate in accordance with working drawings, specifications and manufacturer’s technical data sheet.

Range	eight of – window flashing membranes, building wrap, builder-supplied flashings, timber moisture content, timber deviation, timber treatment, stud spacing, cavity batten layout, foundation alignment, mid-floor alignment, internal corner fixing, control joints.

1.2	Positions of services and fixtures are confirmed to comply with working drawings and job specifications.  All penetrations and projections are confirmed as in place and supported by framing.

Range	three of – downpipes, waste pipes, water taps, collapsible clotheslines, light fittings, telecommunications fixtures, gas fixtures.

1.3	Construction details are checked for compliance with the requirements of the manufacturer for installation of the system, and are confirmed as being in accordance with working drawings.

Range	four of – cavities, ground clearances, junctions, bargeboard clearances, gutter clearances, window clearances, fascia clearance, control joints.

Outcome 2

Describe work necessary to allow the fixing of fibre cement board.

Performance criteria

2.1	Variation in fixing methods and fastener spacing of fibre cement board according to locality and specified wind zone, are described.

Range	sheet edge, building corner, sheet centres, building height.

2.2	Actions to be taken in the event that fixing of the fibre cement board cannot be undertaken in accordance with working drawings, specifications and manufacturer’s instructions are described.

Range	three of – builder, designer, developer, owner, supplier, manufacturer, subcontractor.

Outcome 3

Set up the work area and plan workflow.

Performance criteria

3.1	Area of application is identified in accordance with the plans and specifications.

3.2	Quantities of materials are checked, and are confirmed as being sufficient to complete the job.

3.3	Actions to be taken in the event of insufficient quantities of materials are described.

Range	one of – employer notification, main contractor notification.

3.4	Plant and materials are located in accordance with the required workflow.

Range	three of – scaffold areas, accessibility, services, protection against weather.

3.5	Work of other trades is protected from potential damage due to work activities.

3.6	Access equipment is arranged in accordance with the Health and Safety in Employment Regulations.

Outcome 4

Identify and fix flashings.

Performance criteria

4.1	Proprietary flashings are identified and fixed in accordance with manufacturer’s specifications and job requirements.

Range	four of – head, sill, jamb, parapet, kick-out, control joints, base bead.

4.2	Foamseal flashings are identified and fixed in accordance with manufacturer’s specifications and job requirements.

Outcome 5

Measure, cut and fix fibre cement board.

Performance criteria

5.1	Fibre cement board is measured and marked in accordance with manufacturer’s specifications, job requirements and minimisation of waste.

5.2	Fibre cement board is cut cleanly, to suit the set out, in accordance with job requirements.

5.3	Board edges needing to be jointed are recessed to meet manufacturer’s specifications and are consistent with job requirements.

5.4	Bracing board requirements are identified and fixed in accordance with manufacturer’s specifications and job requirements.

5.5	Fibre cement board is fixed in accordance with manufacturer’s specifications and job requirements.

Range	two of – nails, screws, adhesives, primers.

| Replacement information | This unit standard replaced unit standard 17505. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 January 2006 | 31 December 2024 |
| Review | 2 | 26 January 2007 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.