| Title | Check framing, set up, flash, measure, cut and fix polystyrene board for Proprietary Plaster Claddings on site |
| --- | --- |
| Level | 3 | Credits | 20 |

| Purpose | People credited with this unit standard are able to: check framing on site for suitability for the fixing of specified polystyrene board for an EIFS cladding system; describe work necessary to allow the fixing of polystyrene board; set up work area and plan workflow; identify and fix flashings; and measure, cut, and fix polystyrene board. |
| --- | --- |

| Classification | Construction Trades > Proprietary Plaster Cladding Systems |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Access equipment, for the purpose of this unit standard, means equipment used to facilitate access to the work area, and may include ladders, working platforms, scaffolding or mechanical plant.  Approved codes of practice relating to the safe operation of this equipment are available at https://www.worksafe.govt.nz/.

EIFS means Exterior Insulation and Finishing System.

On site refers to a wide range of building and construction environments within which the Proprietary Plaster Cladding Systems trade skills are applied.

Polystyrene board refers to expanded and extruded types of board.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

2	Legislation, regulations, codes and standards relevant to this unit standard may include:

Health and Safety in Employment Act 1992;

Health and Safety in Employment Regulations 1995;

Resource Management Act 1991;

Hazardous Substances and New Organisms Act 1996; Building Act 2004;

New Zealand Standards, NZS 4218:2004 Energy efficiency – Small building envelope and NZS 3604:1999 Timber Framed Buildings, available from Standards NZ (http://www.standards.co.nz);

New Zealand Building Code;

Approved Code of Practice for the Safe Erection and Use of Scaffolding (Wellington: Occupational Safety and Health Service, Department of Labour, 1995) available at https://www.worksafe.govt.nz/;

Territorial Authorities’ building regulations.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Check framing on site for suitability for the fixing of specified polystyrene board for an EIFS cladding system.

Performance criteria

1.1	Condition of framing is checked on site for suitability for fixing of specified polystyrene board in accordance with working drawings, specifications and EIFS manufacturer’s technical data sheet.

Range	eight of – window flashing membranes, building wrap, builder-supplied flashings, timber moisture content, timber deviation, timber treatment, stud spacing, cavity batten layout, foundation alignment, mid-floor alignment, internal corner fixing, control joints.

1.2	Positions of services and fixtures are checked for compliance with working drawings and job specifications, and services are confirmed as in place and supported by framing.

Range	three of – downpipes, waste pipes, water taps, collapsible clotheslines, light fittings, telecommunications fixtures, gas fixtures.

1.3	Construction details are checked for compliance with the requirements of the EIFS manufacturer for installation of the system, and are in accordance with working drawings.

Range	four of – cavities, ground clearances, junctions, bargeboard clearances, gutter clearances, window clearances, fascia clearance, control joints.

Outcome 2

Describe work necessary to allow the fixing of polystyrene board.

Performance criteria

2.1	Variation in fixing methods and fastener spacing for polystyrene board, according to the specified wind zone, are described.

Range	sheet edge, building corner, sheet centres, building height.

2.2	Actions to be taken in the event that fixing of the polystyrene board cannot be undertaken in accordance with working drawings, specifications and manufacturer’s instructions, are described.

Range	three of – builder, designer, developer, owner, supplier, manufacturer, subcontractor.

Outcome 3

Set up work area and plan workflow.

Performance criteria

3.1	Area of application is identified in accordance with the plans and specifications.

3.2	Quantities of materials are checked, and are confirmed as sufficient to complete the job.

3.3	Actions to be taken in the event of insufficient quantities of materials are described.

3.4	Plant and materials are located in accordance with the required workflow.

Range	three of – scaffold areas, accessibility, services, protection against weather.

3.5	Work of other trades is protected prior to commencement of work.

3.6	Access equipment is arranged in accordance with the Health and Safety in Employment Regulations.

Outcome 4

Identify and fix flashings.

Performance criteria

4.1	Proprietary flashings are identified and fixed in accordance with manufacturer’s specifications and job requirements.

Range	four of – head, sill, jamb, parapet, kick-out, control joints, base bead.

4.2	Fixing blocks and flashings are identified, detailed and fixed in accordance with manufacturer’s specifications and job requirements.

Outcome 5

Measure, cut and fix polystyrene board.

Performance criteria

5.1	Polystyrene board is measured and marked in accordance with manufacturer’s specifications and job requirements.

5.2	Polystyrene board is cut cleanly, to suit the set-out, and is consistent with job requirements.

Range	two of – knives, handsaws, hot wires, hot knives, bench saws.

5.3	Polystyrene board is fixed in accordance with manufacturer’s specifications and job requirements.

Range	nails, screws, adhesives, plaster, proprietary fasteners.

| Replacement information | This unit standard replaced unit standard 17508. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 24 January 2006 | 31 December 2024 |
| Review | 2 | 26 January 2007 | 31 December 2024 |
| Review | 3 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.