| Title | Demonstrate knowledge of and construct curved and sectional moulds for fibrous plaster work in a factory |
| --- | --- |
| Level | 4 | Credits | 8 |

| Purpose | People credited with this unit standard are able to describe methods used to construct curved and sectional moulds for fibrous plaster work; and construct curved and sectional moulds for fibrous plaster work in a factory. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definition

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

2	All work practices must comply with the following:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004; New Zealand Building Code.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Describe methods used to construct curved and sectional moulds for fibrous plaster work in a factory.

Performance criteria

1.1	Methods of constructing curved and sectional moulds are described in accordance with factory requirements and job specifications.

Outcome 2

Construct curved and sectional moulds for fibrous plaster work in a factory.

Performance criteria

2.1	Mould shape is determined from working drawings, job specifications, or sample provided.

2.2	Reverse shape of moulding is set out full size.

2.3	Mould is constructed and finished to give moulding shape.

2.4	Curved plaster moulding is cast to confirm mould profile.

2.5	All operations are completed, workplace, tools and moulds are cleaned, and tools and moulds are stored in accordance with factory requirements.

| Replacement information | This unit standard, unit standard 23534, unit standard 23535, unit standard 23536, and unit standard 23537 replaced unit standard 6131. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 25 January 2008 | 31 December 2024 |
| Review | 2 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.