| Title | Install a manufactured waterproofing system for tiling to wet areas on site |
| --- | --- |
| Level | 4 | Credits | 14 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of manufactured waterproofing systems, select manufactured waterproofing systems for wet area surfaces, prepare wet area surfaces for application of a manufactured waterproofing system on site, install a manufactured waterproofing system on site, and complete work operations. |
| --- | --- |

| Classification | Construction Trades > Floor and Wall Tiling |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

Surfaces refers to walls or floors of concrete, fibre cement, plaster board, timber flooring, tile, acoustic membrane, butyl rubber, rendered surface, cork tile, metal, glass, painted surface, or plastic.  Types of surface may include internal, external, wet, dry, new, existing, painted and unpainted.

Wet area refers to any area exposed to moisture that requires waterproofing, for example bathrooms or laundries.

Work site practice refers to the documented procedures specific to a work site which set out the standard and required practices of that work site.

2	For all on-site unit standards the practical assessment evidence must be provided in the context of commercial business construction operations, in the workplace, under normal workplace conditions.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to work unsupervised, demonstrating knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

4	For the purpose of this unit standard, the surfaces to be tiled must be in wet areas.  Surfaces may include – shower wall, shower floor, bathroom floor.  For assessment against this unit standard, evidence is required of at least two installations, one of which must be a shower.

5	Legislation and publications relevant to this unit standard include:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995;

Building Act 2004;

Resource Management Act 1991;

AS 3958.1:2007, Ceramic tiles - Guide to the installation of ceramic tiles; available from https://www.saiglobal.com/pdftemp/previews/osh/as/as3000/3900/3958.1-2007.pdf.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of manufactured waterproofing systems.

Performance criteria

  - Waterproofing systems are identified and described in terms of types and uses.

Range	negative hydrostatic membranes, positive hydrostatic membranes.

1.2	Selection of a manufactured waterproofing system is explained in terms of connection of membrane to waste.

1.3	Manufactured waterproofing systems are described in terms of suitability for application to substrates.

Range	substrates – plaster board, fibre cement, cement based substrates, plywood.

1.4	Installation of manufactured waterproofing systems, including protection of membrane, is described in accordance with manufacturer’s specifications.

1.5	Testing for watertightness is described in terms of process and manufacturer’s specifications.

Outcome 2

Select manufactured waterproofing systems for wet area surfaces.

Performance criteria

2.1	Waterproofing system is selected in accordance with job specifications and tiling system used.

Outcome 3

Prepare wet area surfaces for application of a manufactured waterproofing system on site.

Performance criteria

3.1	Surfaces to be tiled are identified and checked for compliance with specifications, and actions taken in the event of non-compliance are in accordance with work site practice.

3.2	Method used for preparing surfaces is meets the requirements for surface condition, location, and type of waterproofing system.

3.3	Surface is prepared to a finish suitable for application of the waterproofing system in accordance with specifications.

  - Site is protected against run-off in accordance with legislation.

Outcome 4

Install a manufactured waterproofing system on site.

Performance criteria

  - Waterproofing system is installed in accordance with job and manufacturer’s specifications.

4.2	Waterproofing system is tested for watertightness in accordance with manufacturer’s specifications and work site practice, and watertightness is confirmed.

Outcome 5

Complete work operations.

Performance criteria

5.1	All operations are safely completed; workplace, tools, plant and equipment are cleaned; and tools, plant and equipment are stored in accordance with work site practice.

| Replacement information | This unit standard replaced unit standard 22029. |
| --- | --- |

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 February 2011 | 31 December 2024 |
| Review | 2 | 30 June 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.