| Title | Demonstrate knowledge of applying paint by spray |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | This unit standard is for people working in the painting area of the painting and decorating sector. People credited with this unit standard are able to demonstrate knowledge of: preparing materials and application area for spray painting; setting up and testing spray painting equipment; and applying paint using the spray system. |
| --- | --- |

| Classification | Construction Trades > Painting and Decorating |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Explanatory notes

1	Legislation and references relevant to this unit standard include – Health and Safety in Employment Act 1992; Resource Management Act 1991; Hazardous Substances and New Organisms Act 1996, available at http://legislation.govt.nz; AS/NZS 2311:2009 Guide to the painting of buildings;; AS/NZS 4114.1:2003 Spray painting booths, designated spray painting areas and paint mixing rooms – Design, construction and testing, available at http://www.standards.co.nz/.

2	Definition

Worksite requirements refer to job instructions to candidate on agreed work to be carried out.

Outcomes and evidence requirements

Outcome 1

Demonstrate knowledge of preparing materials and application area for spray painting.

Evidence requirements

1.1	Process for setting up area for spray painting is described in accordance with worksite requirements and the spray system being used.

1.2	Process for protecting adjoining surfaces to application area is described in accordance with worksite requirements.

1.3	Ventilation required for the application area is identified in accordance with worksite and legislative requirements.

1.4	Process for keeping application area free of dust and foreign matter is described in accordance with worksite requirements.

1.5	Materials, plant and tools required to meet the job requirements are identified in accordance with worksite requirements.

1.6	Process for mixing and adjusting paint viscosity, where required, for the application process, is explained in accordance with manufacturer’s specifications and worksite requirements.

Outcome 2

Demonstrate knowledge of setting up and testing spray painting equipment.

Evidence requirements

2.1	Spray painting equipment and accessories are identified in accordance with manufacturer’s specifications and worksite requirements.

2.2	Lines for the spray system are identified so as to contain paint to not reach and penetrate into the skin of workers and other people around them, and are in accordance with manufacturer’s specifications and workplace requirements.

2.3	Process for checking fittings for function and security prior to use is described in accordance with manufacturer’s specifications and worksite requirements.

2.4	Safety devices are identified and process for testing is described in accordance with manufacturer’s specifications and worksite requirements.

Outcome 3

Demonstrate knowledge of applying paint using the spray system.

Evidence requirements

3.1	Process for operating the spray painting equipment is described in accordance with manufacturer’s specifications and worksite requirements.

3.2	Process for applying paint to surface to achieve an even finish is described in accordance with worksite requirements.

3.3	Possible defects in paint application are identified and corrective action to achieve required spray paint finish is described in accordance with worksite requirements.

| Planned review date | 31 December 2019 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 August 2011 | 31 December 2016 |
| Review | 2 | 19 February 2015 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

Please note

Providers must be granted consent to assess against standards (accredited) by NZQA, before they can report credits from assessment against unit standards or deliver courses of study leading to that assessment.

Industry Training Organisations must be granted consent to assess against standards by NZQA before they can register credits from assessment against unit standards.

Providers and Industry Training Organisations, which have been granted consent and which are assessing against unit standards must engage with the moderation system that applies to those standards.

Requirements for consent to assess and an outline of the moderation system that applies to this standard are outlined in the Consent and Moderation Requirements (CMR).  The CMR also includes useful information about special requirements for organisations wishing to develop education and training programmes, such as minimum qualifications for tutors and assessors, and special resource requirements.

Comments on this unit standard

Please contact the Building and Construction Industry Training Organisation info@bcito.org.nz if you wish to suggest changes to the content of this unit standard.