| Title | Maintain a chainsaw |
| --- | --- |
| Level | 3 | Credits | 10 |

| Purpose | People credited with this unit standard are able to: demonstrate knowledge of a chainsaw cutting unit; sharpen a chainsaw chain; and check and maintain a chainsaw. |
| --- | --- |

| Classification | Forestry > Forest Operations |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	A worn chain must be used to demonstrate sharpening.

2	Definition

Accepted industry practice – documented codes of practice and standardised procedures accepted by the wider forestry industry as examples of best practice.

Outcomes and performance criteria

Outcome 1

Demonstrate knowledge of a chainsaw cutting unit.

Performance criteria

1.1	Chain components are identified, and their function described in accordance with accepted industry practice.

Range	cutters, tie straps, drive links, rivets, depth gauges.

1.2	Cutter profiles are identified and compared in terms of use and cutting speed in accordance with accepted industry practice.

Range	chisel, semi-chisel.

1.3	Sprocket sizes are explained in terms of their impact on saw performance.

1.4	The terms pitch and gauge are explained in relation to a chainsaw chain in accordance with accepted industry practice.

1.5	The reasons that cutting unit components must be matched are explained in accordance with accepted industry practice.

Range	sprocket and chain for pitch, bar and chain for gauge.

1.6	Tools for sharpening a chainsaw chain are identified and described in accordance with accepted industry practice.

Range	depth gauge tool, file guide, stump vice, flat file, round file.

1.7	Maintenance requirements of a sprocket tip chainsaw bar are described in accordance with accepted industry practice.

1.8	The main causes of cutting unit faults are identified and corrective maintenance for each fault is explained in accordance with accepted industry practice.

Range	cutting unit faults – cuts are not straight, cutting is aggressive, slow cutting, excessive sawdust, chain overheating, chain locks into sprocket, excessive bar wear, saw jams during cutting.

1.9	Requirements for running in a new chain are explained in accordance with manufacturer’s recommendations.

1.10	Consequences resulting from using a poorly maintained chain are described in terms of effects on operator, maintenance and production.

Outcome 2

Sharpen a chainsaw chain.

Performance criteria

2.1	A location to carry out chainsaw sharpening is selected that is safe, level and clear of natural and operational hazards.

2.2	Chain is sharpened, on the saw, in accordance with accepted industry practice.

Range	tension, file size, use of filing aids, uniform cutter length, file angles, depth gauge settings.

2.3	Sharpened chain is tested in accordance with accepted industry practice.

Range	straight cuts, even cutting, cutting efficiency.

Outcome 3

Check and maintain a chainsaw.

Performance criteria

3.1	Routine checks and maintenance requirements, and their recommended frequency are described in accordance with manufacturer’s recommendations and accepted industry practice.

Range	daily requirements, weekly requirements, monthly requirements.

3.2	Chainsaw is checked and maintained in accordance with accepted industry practice and manufacturer’s recommendations.

Range	air filter, guide-bar, clutch drum bearing, clutch springs, spark plug, cooling system, starter mechanism, spark arrester.

3.3	Tools suitable for chainsaw maintenance are identified and used in accordance with manufacturer’s recommendations.

3.4	Potential causes of chainsaw faults are identified and methods to rectify faults are explained in accordance with accepted industry practice and manufacturer’s recommendations.

Range	chainsaw faults – saw not idling, saw not starting, saw idling too fast, excessive smoke, saw not reaching maximum revolutions, saw not stopping when turned off, chain brake not engaging, chain alternating between loose and tight on the bar, saw stalling.

3.5	Chainsaw is reassembled to safe working condition in accordance with chainsaw manufacturer’s recommendations.

| Planned review date | 31 December 2024 |
| --- | --- |

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 6 September 1993 | 31 December 2011 |
| Review | 2 | 28 September 1995 | 31 December 2011 |
| Review | 3 | 8 November 1996 | 31 December 2011 |
| Revision | 4 | 19 June 1998 | 31 December 2011 |
| Review | 5 | 5 December 2000 | 31 December 2011 |
| Review | 6 | 22 May 2008 | 31 December 2012 |
| Review | 7 | 19 November 2010 | 31 December 2017 |
| Review | 8 | 10 December 2015 | N/A |
| Review | 9 | 26 March 2020 | N/A |

| Consent and Moderation Requirements (CMR) reference | 0173 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.

# Comments on this unit standard

Please contact Competenz qualifications@competenz.org.nz if you wish to suggest changes to the content of this unit standard.