| Title | Construct straight templates and moulds for fibrous plaster work |
| --- | --- |
| Level | 3 | Credits | 10 |

| Purpose | People credited with this unit standard are able to: construct templates for running straight mouldings for fibrous plaster work; construct straight moulds for fibrous plaster work; and clean up after work is completed. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Credit for this unit standard can be achieved on site through a registered assessor, or off site with an accredited training provider.

2	Definition

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following: manufacturer’s specifications or recommendations; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

3	All work practices must comply with the following: Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004;

AS/NZS 2589.2:1997 Gypsum linings in residential and light commercial construction – Application and finishing – Fibre reinforced gypsum plaster, available from Standards NZ (http://www.standards.co.nz); New Zealand Building Code.

Outcomes and performance criteria

Outcome 1

Construct templates for running straight mouldings for fibrous plaster work.

Performance criteria

1.1	Moulding profile is determined from working drawings, and is set out full size in accordance with site practice.

1.2	Template is cut to reverse shape to give required moulding profile for running straight moulds.

1.3	Straight plaster mould is run to confirm mould profile.

Outcome 2

Construct straight moulds for fibrous plaster work.

Performance criteria

2.1	Shape of moulding is identified from working drawings or job specifications.

2.2	Reverse shape of moulding is set out full size and full length in accordance with site practice.

2.3	Mould is constructed and finished to give moulding shape and length, as detailed on drawing.

2.4	All operations are completed without damage to the workplace, tools or plant.

Outcome 3

Clean up after work is completed.

Performance criteria

3.1	Tools and plant are maintained, cleaned and stored in accordance with site practice.

3.2	Waste material is disposed of and workplace is cleaned in accordance with site practice.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 20 April 2006 | 31 December 2024 |
| Review | 6 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.