| Title | Demonstrate knowledge of and cast fibrous plaster sheets in a factory |
| --- | --- |
| Level | 3 | Credits | 8 |

| Purpose | People credited with this unit standard are able to describe methods used to cast, cure and store flat, curved and decorative fibrous plaster sheets; and cast fibrous plaster sheets in a factory. |
| --- | --- |

| Classification | Construction Trades > Fibrous Plaster |
| --- | --- |

| Available grade | Achieved |
| --- | --- |

Guidance Information

1	Definitions

Green sheets means freshly cast sheets of fibrous plaster that have yet to be dried.

Specifications refers to documented instructions (oral, written, graphic) and may include any of the following:  manufacturer’s specifications, recommendations or technical data sheets; material specifications; specifications from a specialist source such as an architect, designer, engineer or a supervisor; site or work specific requirements.

2	All work practices must comply with the following:

Health and Safety in Employment Act 1992 and Health and Safety in Employment Regulations 1995; Resource Management Act 1991; Building Act 2004; New Zealand Building Code.

3	Credit for this unit standard indicates compliance with industry practice.  Industry practice refers to the ability to demonstrate knowledge and skills that reflect the productivity, uniformity, finish quality and material economies currently accepted within industry.

Outcomes and performance criteria

Outcome 1

Describe methods used to cast, cure and store flat, curved and decorative fibrous plaster sheets in a factory.

Performance criteria

1.1	Method of preparing mould and casting is described in accordance with factory requirements.

1.2	Method of curing and storing green sheets is described in accordance with factory requirements.

Outcome 2

Cast fibrous plaster sheets in a factory.

Performance criteria

2.1	Mould is prepared in accordance with manufacturer’s specifications and factory requirements.

Range	two of – flat, curved, decorative.

2.2	Sheet sizes are set out to conform to factory table size.

2.3	Plaster is mixed, and sheets are cast and reinforced in accordance with manufacturer’s specifications and industry practice.

2.4	Green sheets are dried and stored in accordance with factory requirements.

2.5	All operations are completed, workplace, tools and moulds are cleaned, and tools and moulds are stored in accordance with factory requirements.

This unit standard is expiring.  Assessment against the standard must take place by the last date for assessment set out below.

Status information and last date for assessment for superseded versions

| Process | Version | Date | Last Date for Assessment |
| --- | --- | --- | --- |
| Registration | 1 | 18 January 1996 | 31 December 2024 |
| Revision | 2 | 5 July 1999 | 31 December 2024 |
| Review | 3 | 29 August 2000 | 31 December 2024 |
| Revision | 4 | 18 May 2005 | 31 December 2024 |
| Review | 5 | 20 April 2006 | 31 December 2024 |
| Review | 6 | 25 January 2008 | 31 December 2024 |
| Review | 7 | 26 May 2022 | 31 December 2024 |

| Consent and Moderation Requirements (CMR) reference | 0048 |
| --- | --- |

This CMR can be accessed at http://www.nzqa.govt.nz/framework/search/index.do.